## Slide 1: Engineering & Manufacturing Career Pathways
Skills for a future strong workforce

## Slide 2
DMT - Skills for the future
Critical skills for Engineers, Industrial Designers and more
  CAD - Parametric Mechanical Design tools
  3D Printing / Additive Manufacturing “AM”
  Traditional Manufacturing, CNC & CAM

## Slide 3
Charting a pathway to professional success in the 4th Industrial Revolution
AI-driven Generative Design

## Slide 4: DMT Course Summaries
DMT 55 Survey of Design & Manufacturing Processes
DMT 53 Intro to Additive Manufacturing
DMT 54 Product Development with 3D Printing
DMT 56 3D Printing Technician
DMT 57 Design for Additive Manufacturing
Dual Enrollment Program
Additive Manufacturing Technician Certificate

## Slide 5
DMT 55
Survey of Computer Aided Design (CAD), Machining, and 3D Printing
Build insight into how products are designed and fabricated
Explore modern manufacturing processes & equipment
Gain skills in CNC machine setup, blueprint reading, measurement tools, and rapid prototyping
Work on team-based, real-world projects
DMT 55: Survey of Design & Manufacturing Processes

## Slide 6
What you’ll learn
Four weeks: Computer Aided Design (CAD)
3D modeling in SolidWorks, blueprint reading, project workflows, and best practices.
Four weeks: CNC Machining & Measurement
Mill and lathe machining, CNC, and precision measurement tools.
4 weeks: 3D Printing
Two projects using industrial grade 3D printers, slicing software, Design for Additive Manufacturing (DfAM)
DMT 55: Survey of Design & Manufacturing Processes

## Slide 7
What is CAD?
CAD (Computer Aided Design): Software that designers and engineers use for product
development and design.
Helps designers, engineers, architects, and others create accurate 3D models and technical drawings.
Optimize designs – prototypes can be printed, tested, and easily modified in CAD.
Creativity & invention: Bring your own ideas to life
Speaker enclosure printed w/snap-fit joints
The 3D Printing Handbook, pg. 43

## Slide 8: Local companies that use CAD to design products
CAD at De Anza College
Creo Parametric
Autodesk Inventor
SolidWorks
Siemens NX

## Slide 9: Types of Manufacturing
Additive
(e.g., 3D Printing)
Formative
(e.g., Injection Molding)
Subtractive
(e.g., CNC Machining)
  Strong, precise parts
  Limited complexity
  High investment for tooling / setup
  Material waste
  Great for high volume production
  Molding design & fabrication =
  Even higher initial investment
  Affordable at low volume (prototyping)
  “Free Complexity”
  Limitations in strength & precision
  Post-processing required

## Slide 10
www.3dnatives.com/en/mit-10x-faster-3d-printer
additive-vs-subtractive-manufacturing
CAD (Computer Aided Design)
Machining
3D Printing
Subtractive Manufacturing
Additive Manufacturing

## Slide 11
Manufacturing Process
Machining complex parts
Expensive, but strong and precise
3D printing complex parts
Affordable, but reduced strength and precision
Choose the right tool for the job!

## Slide 12
DMT 53
Understand how modern industries use 3D printing in engineering, medicine, product design, and manufacturing
Gain hands-on experience printing with industrial-grade machines
Setup, design, and assess 3D printed parts across major technologies
Discover the latest trends and future technologies in additive manufacturing
DMT 53: Intro to Additive Manufacturing

## Slide 13: DMT Dept’ offers professional engineering pathway skills
3D Printing (“Additive Manufacturing”)
Additive Manufacturing is rewriting the rules for how we design, build, and create in every major industry.
From consumer product and industrial design, automotive, medical to Aerospace industries, the landscape is changing fast and we are here to train the future workforce.
www.deanza.edu/dmt/

## Slide 14
Product Life Cycle: Where does AM fit?
The most effective use of 3D printing technology is at the first and last stages of a product’s life cycle
https://www.maker3d.fi/en/3d-printing-is-best-applied-to-novel-concepts/
3D print value
Product Life Cycle
Mass Production
Production
Ramp Up
Production
Ramp Off
Spare Parts
Production
Functional
Prototypes
Visual
Prototypes
Proof of Concept
Production Tools
(jigs/fixtures)
Quantity
Time

## Slide 15
Vat Photo-polymerization
(Vat Pho or VPP)
Material
Extrusion
(MEX)
Material
Jetting
(MJT)
Binder
Jetting
(BJT)
Powder Bed Fusion
(PBF)
Material (usually melted thermoplastic) is extruded through a nozzle in tracks.
Droplets of photopolymer resin are deposited from nozzles and cured from above with UV light
A vat of photopolymer resin is cured through exposure to UV light,
A bed of powdered material is selectively fused via melting or sintering using a heat source such as a laser.
Liquid binder is applied to a powder bed.
Metal BJT is sintered in a furnace after printing.
Description:
Typical materials:
Thermoplastic filaments such as PLA, ABS, ASA; metal rods, cement, food, etc.
UV curable photopolymer resins and support material
UV curable photopolymer resins
SLS: Thermoplastic powder,
e.g. nylon and TPU
SLM : Metal powder
Plastic & metal powder, ceramics, glass, sand
Alternate Names:
FFF: Fused Filament
Fabrication
FDM: Fused Deposition
Modeling
Polyjet
SLA: Stereolithography
DLP: Digital Light
Processing
mSLA: (LCD) Masked
Stereolithography
CLIP: Continuous Light
Interface Production
BJT: Binder Jetting
MBJ: Metal Binder Jetting
SLS: Selective Laser Sintering
SLM: Selective Laser Melting
EBM: Electron Beam Melting
L-PBF: Laser Powder Bed
Fusion
Process:
Abbreviation:
MJF: Multi Jet Fusion

## Slide 16
3D Printing Technologies @ De Anza
“Additive Manufacturing”
3D Printing Lab
Industry Technologies:
Fused Deposition Modeling (FDM)
HP Multi-Jet Fusion (MJF)
Selective Laser Sintering (SLS)
Bound Metal Deposition
Stereolithography (SLA)
Polyjet

## Slide 17
Powder Bed Fusion
~ Strength & design complexity
Photopolymer Resins
~ Detail & color
~ Medical
FDM / MEX:
Engineering Grade Thermoplastics
Diran 410
3D Printing Technologies @ De Anza

## Slide 18: DMT Dept’ offers professional engineering pathway skills
Dual Enrollment Course HHS
Current high school student can enroll for College credits as a 7th period class
Sign up by contacting your guidance counselor
Email Derek Chan - derek_chan@fuhsd.org
Gain experience with college-level studies
Advance your career and future University prospects at De Anza College
Opportunity to explore potential majors and career paths
DMT 55 starts Sept. 22nd at De Anza College
DMT 53 starts Jan. 5th 2026
www.deanza.edu/dual/fuhsd/
Tiffany Rodriguez-Tran rodrigueztrantiffany@fhda.edu

## Slide 19: Nearly every industry uses CAD & most use 3D Printing
https://www.youtube.com/watch?v=7le2EoJ8b8Q https://youtu.be/A2d96-bCpvo
https://jobs.gecareers.com/global/en/ge-additive-careers https://www8.hp.com/us/en/printers/3d-printers.html

## Slide 20: Nearly every industries uses CAD & Many use 3D Printing
https://www.youtube.com/watch?v=7le2EoJ8b8Q https://youtu.be/A2d96-bCpvo
https://jobs.gecareers.com/global/en/ge-additive-careers https://www8.hp.com/us/en/printers/3d-printers.html

## Slide 21: Universal aspects of all 3D printing
Parts are built Layer by Layer
  3D Geometry is converted to 2D slices, then recompiled during printing
CAD to Print File
  Software translates between your CAD geometry & 3D Printing process (slicing software)
  STL "stereolithography“ file

## Slide 22: Basics of 3D Printing Technology
CAD to Print File, Typically STL or 3MF
Printing Process Mechanism (Pros & Cons)
  FDM/FFF
  SLS, MJF & DLMS
  SLA & DLP
  MJP - Material Jetting
Post Processing
Maintenance and Scalability

## Slide 23: Resent Success story – A vision & passion for success
Dane Jones: https://www.daneerikjones.com/
Chemical Engineering student turned Designer, now works in AM Hardware industry

## Slide 24: Slicing software

## Slide 25: FDM slicing with support structure

## Slide 26: SLA / Vat Pho slicing with support structure

## Slide 27: Considerations when picking print technology
Print Process Mechanism
  How it Works
  Advantages
  Design considerations
FDM / FFF
  Fused Deposition Modeling / Fused Filament Fabrication

## Slide 28: Fused Deposition Modeling / Fused Filament Fabrication FDM / FFF

## Slide 29: Wide range of thermoplastics for FDM PLA, PETG, ABS, PC, PEEK, etc.
FDM typically capable of produces strong part – Engineering grade thermoplastics

## Slide 30: FDM Print Often Requires Support Structures

## Slide 31: FDM is not solid like other processes “Infill & Shell Thickness”
FDM parts are usually not printed solid to reduce the print time and save material.
Instead, the outer perimeter is traced using several passes, called the shell, and
the interior is filled with an internal, low-density structure, called the infill.

## Slide 32: Design considerations for FDM: More significant layer lines compared to SLS, SLA, DLP
It may be difficult to produce parts with fine features, textures or very thin walls

## Slide 33: FDM Parts are generally not watertight or airtight
This issue can be mitigated with post processing but will add time and labor to part

## Slide 34: SLS: Selective Laser Sintering
SLS has becoming more popular and does not require support structures

## Slide 35: SLS: All part geometry's are functionally self-supporting
Unfused power supports parts during printing. Parts can also be nested on top of each other

## Slide 36: 3D Nesting in SLS powder bed fusion “cake”
The unused Nylon power can be recycled for future prints

## Slide 37: SLS: Nylon is ideal for a range of functional applications, from engineering consumer products to healthcare.
SLS 3D Printing Materials
The most common material for selective laser sintering is nylon, a popular engineering thermoplastic beloved for its lightweight, strong, and flexible properties. Nylon is stable against impact, chemicals, heat, UV light, water, and dirt, making it ideal for both rapid prototyping and production.

## Slide 38: Design considerations of SLS, heat up and cool down time.
Warping may occur if insufficient cool down time
Dusty post processing
Fewer material options than FDM
Very durable parts

## Slide 39: SLA & DLP
Photopolymers
DLP is much faster, uses LED projection
SLA finer resolution uses laser
Watertight
Post cure time

## Slide 40: SLA
Very fine resolution 25 micron layers
Liquid Thermoset polymers
watertight parts
Supports are needed to keep build on plate
All layers must have some connections, no island or feathery features without support

## Slide 41: SLA – super fine resolution
Can produce highly detailed & translucent parts

## Slide 42: SLA parts are highly isotropic, watertight parts

## Slide 43: SLA Design considerations; print speed

## Slide 44: Print Speed comparison

## Slide 45: Post Processing considerations

## Slide 46: Support removal – FDM – dissolvable or break away

## Slide 47: Support removal – SLA – break away

## Slide 48: Support removal – SLS powder

## Slide 49: Current Internships, Industry & career connections
Internships & Partners
  Sandia National Laboratories
  Lam Research
  NextFlex
  SME Silicon Valley Chapter 98
    Society of Manufacturing Engineers
    Local Industry tours and networking
    Resume & Career guidance
LinkedIn groups
  CAD
  CNC/CAM/MFG
  3D Printing/AM
DMT Partners
  HAAS
  Siemens
  Autodesk
  SME
www.deanza.edu/dmt/

## Slide 50: Great skills and technical training for a strong future!
3D Printing; Mass is expensive and complexity is free

## Slide 51: This and more at De Anza College in the DMT Dep’t
www.DeAnza.edu/DMT
Build your skills and career opportunities with us now and for the future

## Slide 52
www.deanza.edu/dmt/